## Slide 1: ASTR 2310 General Astronomy I
Professor Mike Brotherton
Ryden & Peterson Chapter 6: Astronomical Detection of Light
The Telescope as a Camera, Refracting and Reflecting, Quality of Images
Instruments and Detectors, Observations and Photon Counting
Observations at Other Wavelengths, Modern Telescopes

## Slide 2: Camera Obscura

## Slide 3: Pinhole Camera
Image is inverted.
Focal length F is length of box
Exposure time can be long since pinhole is small
Exposure time proportional to area of image, or F squared.
Terminology: a short focal length is therefore “fast” and a long one “slow”

## Slide 4: Lenses

## Slide 5: Lenses
Lens is transparent with a refractive index different from air (or surrounding medium).
Refractive index n=c/vm, where vm is the speed of light in the material and c is in a vacuum.
Glass is usually around n=1.5.
Air, n=1.0003

## Slide 6: Snell’s Law

## Slide 7: f-number
Focal length F depends on shape of lens and its refractive index.
Focal ratio f=F/D, where D is diameter of the lens
An f/8 lens has F/D=8.
This basically tells you how “fast” light rays converge.
Can also use f-numbers when discussing mirrors, which we will get to.

## Slide 8: Plate Scale: relating image size to angle

## Slide 9: Plate Scale: relating image size to angle

## Slide 10: Example: The Human Eye
The human eye:
Focal ratio f=F/D, where D is the diameter of the lens
Bright surroundings, f/8
In the dark, f/2

## Slide 11: The Powers of a Telescope (I): Size does matter!
1. Light-gathering power: Depends on the surface area A of the primary lens / mirror, proportional to diameter squared:
A =  (D/2)2
D

## Slide 12: The Powers of a Telescope (II)
2. Resolving power: Wave nature of light => The telescope aperture produces fringe rings that set a limit to the resolution of the telescope.
min = 1.22 (/D)
Astronomers can’t eliminate these diffraction fringes, but the larger a telescope is in diameter, the smaller the diffraction fringes are. Thus the larger the telescope, the better its resolving power.
For optical wavelengths, this gives
min = 11.6 arcsec / D[cm]
min

## Slide 13: Diffraction Limited Image Resolution
The “Airy disk” is the bright central region of the ringed pattern from a point source through a circular aperture.

## Slide 14: Astronomical Seeing

## Slide 15: Seeing
Weather conditions and turbulence in the atmosphere set further limits to the quality of astronomical images
Bad seeing
Good seeing

## Slide 16: The Best Location for a Telescope (I)
On high mountain-tops – to avoid atmospheric turbulence ( seeing) and other weather effects
Paranal Observatory (ESO), Chile
http://en.wikipedia.org/wiki/Paranal_Observatory

## Slide 17: The Best Location for a Telescope (II)
Far away from civilization – to avoid light pollution

## Slide 18: Refracting Telescopes (lenses)

## Slide 19: Refracting Telescopes (lenses)
Chromatic aberration: Different wavelengths are focused at different focal lengths (prism effect).
Can be corrected, but not eliminated by second lens out of different material.
Difficult and expensive to produce: All surfaces must be perfectly shaped; glass must be flawless; lens can only be supported at the edges.

## Slide 20: Lick 36” Refractor (1888)
Hard to build lenses (f/19) much bigger!
First Mountaintop Telescope
Nice to look through for your guests at a wedding reception.
"Here lies the body of James Lick".

## Slide 21: Amazing History of the Telescope
Nice video (12 minutes) about historical telescope development through the nineteenth century. Pretty cool stuff! Watch outside of class, please.

## Slide 22: Reflecting Telescopes (mirrors, now standard)

## Slide 23: WIRO 2.3-m (1977)

## Slide 24: Refracting / Reflecting Telescopes
Refracting Telescope: Lens focuses light onto the focal plane
Reflecting Telescope: Concave Mirror focuses light onto the focal plane
Almost all modern telescopes are reflecting telescopes.
Focal length
Focal length

## Slide 25: Secondary Optics
In reflecting telescopes: Secondary mirror, to re-direct light path towards back or side of incoming light path.
Eyepiece: To view and enlarge the small image produced in the focal plane of the primary optics.

## Slide 26: Reflectors: some optical configurations

## Slide 27: Image Quality Issues with Optical Systems
Spherical aberration: different annuli of lens or mirror have different focal lengths, therefore not one clean focal plane.
Coma: Light rays near edge of lens/mirror come to a focus at a larger distance than those near the center (seen in off-axis images from parabolic mirrors).
Astigmatism: Happens when radius of curvature differs along different axes.
Curvature of field: Detectors usually flat, but real focal surface is not a plane, but curved, in practice.
Distortion: pincushion (positive), barrel (negative).

## Slide 28: Image Quality Issues with Optical Systems

## Slide 29: Image Quality Issues with Optical Systems

## Slide 30: Image Quality Issues with Optical Systems

## Slide 31: Image Quality Issues with Optical Systems

## Slide 32: Image Quality Issues with Optical Systems

## Slide 33: Advances in Modern Telescope Design
Lighter mirrors with lighter support structures, to be controlled dynamically by computers
Floppy mirror
Segmented mirror

## Slide 34: Adaptive Optics – Ground-based telescopes
Computer-controlled mirror support adjusts the mirror surface (many times per second) to compensate for distortions by atmospheric turbulence

## Slide 35: Point Spread Function or PSF